## Slide 1
LEADER DECISION / CURRENT FLOW
Leader Decision은 mission 선택과 safety 선점을 분리한다
Perception/GPS/Planning 입력을 받아 주행 상태를 정하고, 위험 신호는 모든 mission 위에서 throttle을 0으로 선점한다.
GP_Decision
Leader vehicle driving scope
Perception context
/drive_context
/traffic_stop, /intersection
/roi_warning
GPS / Localization
/csv_path
TF: csv → vehicle_ref
/vehicle_heading_valid
Planning command
/throttle_from_planning
Highway or Complex source
>
context
>
pose/path
>
planning
mission_supervisor_node
preemptive state machine
Mission layer
/drive_context → HIGHWAY / CITY / COMPLEX
active_algorithm과 mission별 throttle policy 결정
Safety layer
/manual_stop, /safety_stop
/traffic_stop && /intersection
/roi_warning → throttle_cmd = 0
safety has priority over every mission state
>
status
>
cmd
State visibility
/mission_state
/active_algorithm
/safety_status, /safety_active
Vehicle command
/throttle_cmd
planning throttle passes through only when safety is clear
mission별 속도 정책
HIGHWAY
GPS path tracking / scale 1.0, limit 0.7
CITY
GPS tracking + low-speed policy / scale 0.75, limit 0.5
COMPLEX
GPS targeting + local planner policy / scale 0.6, limit 0.4
Sources: README.md, mission_supervisor_logic.py, mission_supervisor.yaml
1 / 2

## Slide 2
COMPLEX FLOW / 1ST INTEGRATION
Complex에서는 GPS가 목표를 주고 LiDAR/RRT가 local path를 만든다
Highway와 Complex planning command는 command_mux에서 선택되고, 최종 throttle은 mission_supervisor의 safety gate를 지난다.
Complex lane
CSV path + TF
전역 GPS path
vehicle_ref 변환
complex_target
/csv_path →
/complex/rrt_target
RRT planner
cone obstacle + target
RRT/corridor branch
→ /complex/local_path
Complex PP
local path 추종
steer + throttle
>
>
>
Highway lane
ROI path
전방 ROI 생성
/roi_path
pure_pursuit
Highway GPS tracking
/highway/* command
>
command_mux
mission_state 또는
/drive_context 기준 선택
Supervisor
safety 선점 후
/throttle_cmd 출력
>
v
>
/auto_steer_angle
/throttle_from_planning
/planning_command_source
vehicle_ref 기준 Complex local view
GPS는 목표점, LiDAR/RRT는 실제 local path
Leader
RRT target
LiDAR cone map
/complex/local_path
1. GPS long-range intent
CSV path에서 전방 RRT target 생성
2. LiDAR local evidence
cone/detected_objects를 obstacle로 사용
3. Shared command gate
mux 선택 뒤 supervisor safety 선점
Sources: README.md, planning_single_f9p.launch.py, complex_target_node.py, complex_rrt_planner_node.py, command_mux_node.py
2 / 2